## Slide 1: WIEGMANN
NEMA 101 Training
June 4th, 2020
Travis Miller

## Slide 2: AGENDA
What is NEMA
What Are the Different NEMA Enclosure Types
What NEMA Types Does WIEGMANN Offer
Other Products
Other Standards

## Slide 3: What Is NEMA
National Electrical Manufacturers Association
Purpose Is To Improve The State Of Electrical Manufacturing In The United States.
  350 Member companies
  Publishes 700+

## Slide 4: What Is NEMA
NEMA Enclosure Types
  NEMA defines standards used in North America for various grades of electrical enclosures typically used in industrial applications. Each is rated to protect against personal access to hazardous parts, and additional type-dependent designated environmental conditions. A typical NEMA enclosure might be rated to provide protection against environmental hazards such as water, dust, oil, coolant, or atmospheres containing corrosive agents.

## Slide 5: NEMA Enclosure Types
Type 3S
Type 4
Type 4X
Type 5
Type 6
Type 6P
Type 12/K
Type 13
Type 1
Type 2
Type 3
Type 3R/X

## Slide 6: WIEGMANN / NEMA
Type 3S
Type 4
Type 4X
Type 5
Type 6
Type 6P
Type 12/K
Type 13
Type 1
Type 2
Type 3
Type 3R/X

## Slide 7: WIEGMANN / NEMA
Type 3S*
Type 4
Type 4X
Type 5
Type 6
Type 6P*
Type 12/K
Type 13
Type 1
Type 2
Type 3
Type 3R/X
* Type 3S and 6P are only available in Non-Metallic

## Slide 8: NEMA 1
Indoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Falling dirt
Designated by “SC” “A” “N1C”
S

## Slide 9: NEMA 3RX
Indoor or Outdoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Falling dirt
    Dripping/light splashing water
Designated by “RSC” “RHC” “LOH” “WCT” “CT”

## Slide 10: NEMA 3RX
Indoor or Outdoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Falling dirt
    Dripping/light splashing water
    X – signifies corrosion protection
Designated by “RSC_NKSS”
S

## Slide 11: NEMA 4
Indoor or Outdoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Windblown dust, rain, sleet, snow
    Hose directed Water
    Undamaged by ice forming on the surface
Designated by “BN4” “Ultimate” “WA_GSC” “N412_C” “N4” “WRD”

## Slide 12: NEMA 4X
Indoor or Outdoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Windblown dust, rain, sleet, snow
    Hose directed Water
    Undamaged by ice forming on the surface
    X – signifies corrosion protection
Designated by “BN4” “WA_GSC” “N412_C” with “SS” “SSA” or “AL” at the end

## Slide 13: NEMA 12
Indoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Windblown dust, rain, sleet, snow
    Oil and Coolant Seepage
Designated by “B_/CH” “N12” “WA_WF/FS/FSD/FSDA/FSDAD/E”

## Slide 14: NEMA 13
Indoor Use
  Protects user from contact.
  Protects components from:
    Ingress of solid objects
    Windblown dust, rain, sleet, snow
    Oil and Coolant Seepage
    Oil and Coolant Spay/Splash
Designated by “B_/CH/CHQR/SC/CHFTC” “WA_GIE” “WA_FM” “N12”

## Slide 15: Other Products
Wireway / Fittings/ Troughs
Non-Metallic
Back Panels
Disconnects

## Slide 16: NEMA Summary

## Slide 17: Additional Standards
Some Products Meet Multiple NEMA Ratings
Other National And International Standards May Also Apply

## Slide 18: NEMA vs IEC
IEC is the primary stand used in Europe

## Slide 19: QUESTIONS?